## Slide 1: 3D Computer Modeling
Using Inventor

## Slide 2: 3D Modeling in Inventor
Getting Started
This is what you will see when you first open Inventor.
You can begin a new file or open an existing file with either the New or Open commands on the Launch panel, the Quick Access Toolbar, or the Application Menu.
When selecting New, be sure to choose the correct system, either English or Metric.
Notes: .idw stands for Inventor drawing file
.iam stands for Inventor assembly file
.ipt stands for Inventor part file
.ipn stands for Inventor presentation file

## Slide 3: Inventor Screen Layout
Application Menu
  Contains common commands for creating, saving, and printing.
Quick Access Toolbar
  Provides quick access to frequently used commands
Ribbon
  A palette that displays buttons and controls used for both 2D drawing and annotation and 3D modeling and viewing
Ribbon Tabs
  Organized by task, contain task specific buttons and controls
Graphics Window
  The active modeling area where parts and assemblies are created and edited
Application Menu
Quick Access Toolbar
Graphics
Window
Ribbon Tabs
Ribbon
Notes: Show students how to use the help command to find answers to their questions.

## Slide 4: Inventor Screen Layout
View Cube
  Clickable and draggable interface that is used to switch between standard and isometric views
Navigation Bar
  On screen element that provides access to various navigation tools
Browser
  Maintains history of part, assembly, or drawing creation
  3D Indicator
  Shows direction of X, Y, and Z coordinates.
  Red represents X,
  Green represents Y
  Blue represents Z directions
Browser
3D Indicator
View
Cube
Navigation Bar

## Slide 5: Mouse Buttons
Left Mouse Button
  Used to select icons, menus, and graphics
Right Mouse Button
  Brings up additional options
  Accepts default option
  Ends a process
Middle Button/Wheel
  Provides quick pan and zoom functions
Notes: Demonstrate that ESC on the keyboard cancels a command.

## Slide 6: Geometric Constraints
Symbols that show alignments to capture the design intent
To use Geometric Constraints:
2. Right mouse click in Graphics Window, then select Create Constraint
OR
1. Use the commands available from the Sketch panel
Notes: Students should experience sketching in the 3D Modeling software before you discuss this slide. Ask whether they noticed symbols that appeared as they sketched. These clues or symbols show alignments or constraints that the software assumes you want. If you don’t want these constraints, press the Ctrl key, and the inferred constraint will not be created.

## Slide 7: Geometric Constraint Symbols
 | Perpendicular | Lines are at right angles
 | Parallel | Line is parallel to other objects
 | Tangent | Touches at one point only
 | Smooth | Create a continuous curve
 | Coincident | Constrains 2 points or point to curve
 | Concentric | Arc or Circle shares center point
 | Collinear | 2 lines lie along the same line
 | Equal | Resizes to same radius or length
 | Horizontal | Line is parallel to X axis
 | Vertical | Line is parallel to Y axis
 | Fix | Points or curves stay locked in place
 | Symmetry | Objects align symmetrically about a line

## Slide 8: Dynamic Viewing Functions
 | Pan
 | Zoom
 | Zoom Window
 | Zoom All
 | Zoom Selected
 | Dynamic Rotation
 | Look At
Located on View Ribbon Tab
Used to Zoom and Pan to reposition the sketch
Notes: The teacher will demonstrate and students should practice using all of the dynamic viewing functions.

## Slide 9: Precise Input
The Precise Input toolbar is added by expanding the Draw panel and selecting Precise Input
Create the shapes that you labeled in Activity 1.5.1 The Coordinate System and Descriptive Geometry.
Notes: Precise Input using Relative Coordinates
Precise input is a method used to plot coordinates. Precise input allows the user to specify precise coordinates when creating a sketch. You can enter coordinates to specify the location for a point.

## Slide 10: Image Resources
Microsoft, Inc. (2008). Clip Art. Retrieved November 4, 2008, from http://office.microsoft.com/en-us/clipart/default.aspx